## Slide 1: Real-time data in Intermagnet
Simon Flower

## Slide 2
Real-time data in Intermagnet
What are we doing and what progress have we made?
Monitoring Intermagnet’s real-time data
What next?
Introduction

## Slide 3: Intermagnet data transport (2024)
Paris
Kyoto
Golden
Ottawa
Edinburgh
Other Intermagnet observatories
US Observatories
Canadian Observatories
Email
Email
Email
Web service
Rsync
Rsync
Rsync
Rsync

## Slide 4: Faster Intermagnet data transport (2026?)
Web service
Paris
Kyoto
Golden
Ottawa
Edinburgh
Other Intermagnet observatories
US Observatories
Canadian Observatories
Email
Email
Email
Seedlink
Seedlink
MQTT
MQTT
MQTT
MQTT
MQTT

## Slide 5: Progress – the Edinburgh GIN
Edinburgh
Seedlink
Seedlink
MQTT
MQTT
MQTT
Seedlink ingestion to GIN tested and running
MQTT broker installed
MQTT ingestion to GIN tested and running
Real-time performance monitoring system created
Complete

## Slide 6: Progress – other GINs
Paris
Kyoto
Golden
Ottawa
Seedlink
Seedlink
MQTT
MQTT
GIN | Rsync Replacement | Progress
Golden | Seedlink | Seedlink server available
Ottawa | Seedlink | 
Kyoto | MQTT | First MQTT service by end of 2025
Paris | MQTT | Planning replacement of GIN
MQTT
MQTT
Complete

## Slide 7: Progress – observatories
Paris
Kyoto
Edinburgh
MQTT
MQTT
MQTT
MQTT
MQTT
Observatories using MQTT: 6 (BEL, DOU, HLP, HRN, MAB, VAL)
Other Intermagnet observatories

## Slide 8: What’s still needed
Golden GIN | Make data available via Seedlink (or MQTT) to Edinburgh GIN
Kyoto GIN | Complete work on replacing Rsync with MQTT Encourage observatories to increase frequency of data transmission
Paris GIN | Start work on replacing Rsync with MQTT Encourage observatories to increase frequency of data transmission
Observatories | We all need to encourage observatories to speed up their data flow
Observatories don’t need to use MQTT to make faster transfers (though MQTT is a good choice).
MQTT by itself won’t make for faster data – it’s the rate at which data is sent (over whichever transport an observatory chooses) that’s important.

## Slide 9
Data lag times consist of the difference between the current time and the time of the most recently recorded data sample. These have been recorded once a minute at the Edinburgh GIN for all observatories since May 2024.
To monitor network performance:
The lag times are retrieved for a given time span.
A percentage of the largest (worst) lag times are removed, to prevent unusual data transmission problems affecting the results.
The minimum, median and maximum lag times are found, for each observatory, from the remaining data.
The minimum, median and maximum lag times are grouped into "bins" (by default 2 mins, 3 mins, 4 mins, 5 mins, 30 mins, 1 hour, 12 hours, 1 day, 3 days).
https://imag-data.bgs.ac.uk/GIN_V1/WebServiceURLGenerator.jsp#network_performance_service
Monitoring progress - network performance

## Slide 10
Data cadence: minute Discard percentage: 10%
Maximum lag time |  | Observatories | List of observatories
[0,2] | (2 mins) | 0 | 
[3] | (3 mins) | 4 | ESK, HAD, LER, OTT
[4] | (4 mins) | 0 | 
[5] | (5 mins) | 1 | CNB
[6,10] | (10 mins) | 35 | ASC, ASP, BLC, BOU, BRW, BSL, CKI, CMO, CSY, CTA, DOU, FCC, FRD, FRN, FUR, GNG, GUA, HON, IQA, JCO, KDU, LRM, MAB, MAW, MCQ, MEA, NEW, NUR, PST, RES, SHU, SJG, STJ, TUC, YKC
[11,30] | (30 mins) | 20 | ARS, BEL, GDH, HLP, HRN, HYB, KAK, KNY, MMB, NAQ, NGK, PAG, SPT, SUA, TTB, VIC, VNA, VSS, WIC, WNG
[31,60] | (1 hr) | 12 | ABK, BFO, GAN, KIR, LON, LYC, SHE, SOD, STT, TDC, UPS, VOS
[61,720] | (12 hrs) | 7 | API, BDV, EYR, IZN, SBA, SBL, THY
[721,1440] | (1 day) | 16 | BMT, BRD, CBB, CLF, CYG, DED, DLT, EBR, KEP, KOU, NCK, PHU, PPT, SIT, TAM, THL
[1441,4320] | (3 days) | 11 | ABG, DUR, GCK, HRB, IPM, IRT, JAI, LVV, ORC, PIL, SFS
>4320 | (>3 days) | 25 | AIA, BFE, BOX, CNH, CPL, GNA, GUI, HBK, HER, HUA, ISK, KHB, KIV, KMH, MGD, MZL, NVS, PAF, PEG, PET, SPG, TSU, VAL, WMQ, YAK
Network performance – August 2024

## Slide 11
Data cadence: minute Discard percentage: 10%
Maximum lag time |  | Observatories | List of observatories
[0,2] | (2 mins) | 1 | STJ
[3] | (3 mins) | 3 | HAD, LER, OTT
[4] | (4 mins) | 2 | DED, ESK
[5] | (5 mins) | 1 | BSL
[6,10] | (10 mins) | 34 | ASC, ASP, BLC, BOU, BRD, BRW, CBB, CKI, CMO, CNB, CSY, CTA, FCC, FRD, FRN, GNG, GUA, HON, IQA, JCO, KDU, LRM, MAW, MCQ, MEA, NEW, PST, RES, SBL, SHU, SIT, SJG, TUC, YKC
[11,30] | (30 mins) | 11 | CLF, DLT, DOU, IPM, KAK, KNY, MAB, MMB, PPT, SUA, VIC
[31,60] | (1 hr) | 9 | BFO, GAN, SHE, STT, TDC, TTB, VNA, VOS, VSS
[61,720] | (12 hrs) | 15 | ABK, API, ARS, BDV, EYR, GDH, KEP, KOU, LYC, NAQ, SBA, SOD, SPT, THL, UPS
[721,1440] | (1 day) | 3 | HLP, SFS, TAM
[1441,4320] | (3 days) | 19 | AIA, BEL, CPL, FUR, GCK, GUI, HRB, HYB, IRT, JAI, LON, LVV, NGK, NVS, ORC, PAG, PIL, VAL, WNG
>4320 | (>3 days) | 33 | ABG, BFE, BMT, BOX, CNH, CYG, DUR, EBR, GNA, HBK, HER, HRN, HUA, ISK, IZN, KHB, KIR, KIV, KMH, MGD, MZL, NCK, NUR, PAF, PEG, PET, PHU, SPG, THY, TSU, WIC, WMQ, YAK
Network performance – August 2025
Notes: Canadian GIN change from Rsync to Seedlink occurred 19th August 2025

## Slide 12: What do we want to do next?
Intermagnet observatories
Intermagnet GINs: real-time data available
Real-time transport
Geomanetic applications

## Slide 13: What do we want to do next?
Intermagnet observatories
Intermagnet GINs: real-time data available
Users
Real-time transport
??
How do we get data to users in real-time?
How do we do this efficiently?
Intermagnet: standards based real-time data (e.g. web services, MQTT)
Then anyone, inside or outside Intermagnet, can make applications
Geomagnetic applications